## Slide 1
OPL for Esilicon MI5 Wafer Out of Cassette Slot
Customer | Esilicon / 77 | P/D/L | 12” wafer | MM/D,W,S | 11/18/2019 | Lot # | N33R06.00
Defect | Wafer Out of Cassette Slot |  | Defect Ratio | 5.88% (1/17) |  | Status# | Hold at OQA Gate
Possible Root Cause:
  Esilicon feedback some shipped wafer have discolor issue, so we picked up some wafer in ATC line to check if any similar discolor issue, including this lot N33R06.00. But CP line has no 12” OM tool, so the wafer was picked out and checked under microscope manually. Impacted wafer was not put in correct position when return back to the cassette.
Problem Description:
One wafer was found out of cassette slot during CP OQA gate, it would have high risk of wafer broken in later process, This lot is on hold waiting for disposition.
Action Plan:
  Order new 12” OM tool for the incoming and outgoing inspection, to eliminate all manual job.
  Resp: Heaton Ge/Chen Jun Due Date: 02/29/2020 Status: Ongoing(PR already issued, 3 month build time)
  Before CP 12”OM ready, define procedure that use Bump machine for marco inspection of CP 12” lots.
  Resp: Yaping Zhu Due Date: 11/27//2019 Status: On-going
Notes: This is a Title and Content slide.