## Slide 1
OPL Intel Re-burn Over Stress
Customer | Intel / 126 | P/D/L | 5J/1F/132 4P/1A/132 | MM/D,W,S | 08/31/2020 | Lot # | S035C040/S035C065/S035C064
Defect | Re-burn over stress |  | Defect Ratio | 3 lots/ 18000ea units |  | Status# | Bin Reclaim
Possible Root Cause:
Engineer need modify ATT file manually before re-burn.
As these lots were hard stopped during cold testing, engineer add special color for these lots in tracking list and filter out these lots when doing attribute file modification. Missing att file modification for these lots by mistake
Current system did not support ATT file auto update for Re-BURN lots
Problem Description:
Engineer detected that three lots re-burned with original ATT file by mistake without adding “abort_st=STC/STE” as instructed by intel TE though call.
Action Plan:
Optimize work flow for re-burn lots disposition, any manual ATT file modification required 2nd PE cross check
  Resp: ATC PE Due Date: 9/11/2020 Status: Ongoing
Proposal to intel team: to use treadstone to pass Re-burn attribute to ATC system , then ATC system can generate re-burn ATT file automatically
  Resp: Intel/ATE Due Date: TBD Status: Ongoing
Intel PC
  Tread stone [IMFT_Attribute_Report] to add one attribute named “abort_st”, default value is blank
ATC PE
  Report SBL triggered Lot OR abnormal lots in ILM
Intel PE
  Provide lot disposition through ILM
  Update attribute “abort_st” value through treadstone
ATC PE
  Received disposition in ILM and refresh ATT file for Re-BURN lots
  System auto got “abort_st” value through IMFT_Attrubute_Report
ATCLot | CusLotNum | FabLotNbr | TargetDevice | Oper | Qty | Bin1 | Yield | Intel Disposition through call | Re-Burn Attribute Used
FTL356675778.01 | S035C065 | K0215990 | N18A-22FF-C522 | BURN IN | 6,000 | 5913 | 98.55% | ATT file add abort_st=STC | Original ATT file
FTL356675746.01 | S035C040 | K0215100 | N18A-22FF-C522 | BURN IN | 6,000 | 5912 | 98.53% | ATT file add abort_st=STC | Original ATT file
FTL356675896.01 | S035C064 | K0238000 | B17A-82FF-C538 | BURN IN | 6,000 | 5761 | 96.02% | ATT file add abort_st=STE | Original ATT file
Notes: This is a Title and Content slide.