## Slide 1
Notes: This is the First Slide of each and every presentation.

## Slide 2
Sorter
OI
Sorter handler
assy1.asc(OI create)
asmb1.asc(OI create)
PKGID.csv(OI create)
Lot information
Handler summary
System
Each single lot
summary
OI function:
1,Get lot information from system to create assy1,asmb1 file ,search related PKGID.csv file, send these 3 files to handler.
2,Get handler summary ,analysis, create each single lot summary and send to system.
3,Create lot history file(testtime_log)

## Slide 3
ATC Lot No
ok
Key No
Operator ID
Test Start
Cancel test
Sorter OI
Lot track in
OP input Lot No
OI get key No and show
Click ok
OP Input operator ID
Click test start
Lot test
Click Lot End
Node 1
Lot track out
Node 2
Node 4
Next process
Work flow
OI interface
ok
ok
ok
NG
NG
NG
alarm
alarm
alarm
Retest Start
Lot End
Assy1.asc
Asmb1.asc
PKGID.csv
Click retest start
NG
alarm
Node 3
Lot need retest
Lot end
ok
Lot retest

## Slide 4
Node 1
Warning!
Can’t get lot information, please check.
OK
After click ok, OI will search Lot information(combine lot key no ; sub lot lot no & key no; process; combine lot and sub
lot quality,2DID) by lot no in AMS, at the same time ,create assy1.asc/asmb1.asc/PKGID.csv file. if OK, OI will show key
no information and 3 files create ok information, if NG, alarm.
VC4347VC3831
ATC Lot No
ok
KP1912
Key No
Operator ID
Test Start
Cancel test
Sorter OI
Retest Start
Lot End
Assy1.asc
Asmb1.asc
PKGID.csv
√
√
√

## Slide 5
Node 1 – 3 files create rule
Example-- Lot No:VC4347VC3831/Key No:KP1912
Keyno000.00&(000.00& is fixed format)
LOT1000.00&LOT2000.00&Z99999999.99&Z99999999.99&Z99999999.99&(000.00& is fixed format, total 5 lots, if just 2 or 3 lot, the rest lot use Z99999999.99&)
Lot1 key no
Lot2 key no
2DID

## Slide 6
Node 2
Warning!
Send xxxxx file fail, please check.
OK
After click start test, OI will send assy1.asc&asmb1.asc&PKGID.csv 3 files to handler. If ok, pop up success ,after click ok, handler can start test, If NG , alarm.
Success!
OK

## Slide 7
Node 3
Warning!
Send xxxxx fail, please check.
OK
If lot need retest, click retest start, OI will send retest signal to handler. If ok, pop up success ,after click ok, handler can start test, If NG , alarm.
Note: In initial test, the flag is INI, after click retest start, the flag is RT1, click retest start again, the flag is RT2.
Success!
OK

## Slide 8
Node 4
Warning!
Can’t create/send xxxxx file, please check.
OK
After OI get lot end single, OI pop up a windows(Lot end), OP click ok , then click Lot end on OI, OI will carry out 2 action:
1,get summary from handler and analysis, create each sub lot summary, pop up summary of combine lot(OP can compare
Quality with device in handler).---refer to page9,10,11
2,Create testtime_log and test_log (If happened problem, we can check history).--refer to page12,13
If all ok, pop up windows success, after click ok, OI will clear the information on OI. Next lot can start, any NG, alarm.
Lot end!
OK
Success!
OK

## Slide 9
Node 4-1 Summary
Split method:
Combine lot bin information should have bin1,bin2,bin3,bin4,other.sub lot bin information should have bin1,other
SORT1 sum quality=combine lot bin1 quality=sub lot1 bin1 quality
SORT2 sum quality=combine lot bin2 quality=sub lot2 bin1 quality
SORT3 sum quality=combine lot bin3 quality=sub lot3 bin1 quality
SORT4 sum quality=combine lot bin4 quality=sub lot4 bin1 quality
SORT5 sum quality=combine lot other quality
Sub lot1 other quality=sub lot1 track in quality(AMS)-sub lot1 bin1 quality
Sub lot2 other quality=sub lot2 track in quality(AMS)-sub lot2 bin1 quality
Sub lot3 other quality=sub lot3 track in quality(AMS)-sub lot3 bin1 quality
Sub lot4 other quality=sub lot4 track in quality(AMS)-sub lot4 bin1 quality
Storage path: D:\Datalogs
File format: LOTNO_PROCESS_end_INI.asc
(LOTNO; PROCESS get from AMS; end is fixed format; INI is flag: if initial test , it’s INI, if first retest, it’s RT1, all sub lot flag use combinelot flag )
Storage method: Saved in local D:\Datalogs and upload to \\c3nas03\Data\737\Combine_lot_result_file
Handler summary

## Slide 10
Node 4-1 Summary
SORT1 sum quality=combine lot bin1 quality=sub lot1 bin1 quality
SORT2 sum quality=combine lot bin2 quality=sub lot2 bin1 quality
SORT3 sum quality=combine lot bin3 quality=sub lot3 bin1 quality
SORT4 sum quality=combine lot bin4 quality=sub lot4 bin1 quality
SORT5 sum quality=combine lot other quality
Sub lot1 other quality=sub lot1 track in quality(AMS)-sub lot1 bin1 quality
Sub lot2 other quality=sub lot2 track in quality(AMS)-sub lot2 bin1 quality
Sub lot3 other quality=sub lot3 track in quality(AMS)-sub lot3 bin1 quality
Sub lot4 other quality=sub lot4 track in quality(AMS)-sub lot4 bin1 quality
Example-- Lot No:VC4347VC3831/Key No:KP1912
Combine lot summary file
HDL,lot no,lotno,keyno,bin1,bin2,bin3,bin4,bin5,bin6,bin7,bin8,bin9,other,process(bin5-9=0)
Sub lot1 summary file
HDL,lot no,lotno,keyno,bin1,bin2,bin3,bin4,bin5,bin6,bin7,bin8,bin9,other,process(bin2-9=0)
Sub lot2 summary file
HDL,lot no,lotno,keyno,bin1,bin2,bin3,bin4,bin5,bin6,bin7,bin8,bin9,other,process(bin2-9=0)

## Slide 11
Node 4-1 Summary --If Retest
Lot no | Keyno | Flag | QTY IN | Bin1 | Bin2 | Bin3 | Bin4 | Bin5 | Bin6 | Bin7 | Bin8 | OT
VC4347VC3831 | KP1912 | INT | 500 | 180 | 280 |  |  |  |  |  |  | 40
Lot no | Keyno | Flag | QTY IN | Bin1 | Bin2 | Bin3 | Bin4 | Bin5 | Bin6 | Bin7 | Bin8 | OT
VC4347VC3831 | KP1912 | INT | 500 | 180 | 280 |  |  |  |  |  |  | 40
VC4347VC3831 | KP1912 | RT1 | 40 | 15 | 15 |  |  |  |  |  |  | 10
Lot no | Keyno | Flag | QTY IN | Bin1 | Bin2 | Bin3 | Bin4 | Bin5 | Bin6 | Bin7 | Bin8 | OT
VC4347VC3831 | KP1912 | INT | 500 | 180 | 280 |  |  |  |  |  |  | 40
VC4347VC3831 | KP1912 | RT1 | 40 | 15 | 15 |  |  |  |  |  |  | 10
VC4347VC3831 | KP1912 | RT2 | 10 | 2 | 3 |  |  |  |  |  |  | 5
Just initial test
Retest once
Retest twice
INI BIN1+RT1 BIN1
INI BIN2+RT1 BIN2
RT1 OT
INI BIN1+RT1 BIN1+RT2 BIN1
INI BIN2+RT1 BIN2+RT2 BIN2
RT2 OT

## Slide 12
Node 4-2 testtime_log
Storage path: D:\testtime_log
File format: testtime_yymmdd.log
Rule: Create one file a day, daily content is recorded inside
[Lot Start],start test time,lotno,keyno,operatorID
[Lot End],cancel test time,lotno,keyno, operatorID

## Slide 13
Node 4-2 test_log
Storage path: D:\test_log
File format: testlog_yymmdd.log
Rule: Create one file a day, daily content is recorded inside
Content: communication with OI and handler

## Slide 14
Node 5 Cancel test
If lot happened any problem need cancel test, click cancel test , OI will empty current information.

## Slide 15
Thank You